## Slide 1
Refraction and Snell’s Law
Outline
TE and TM fields
Refraction and Snell’s Law:
- From TE analysis
- From Phase Matching
- From Fermat’s Principle of Least Time
Total Internal Reflection and Fibers
FIOS
Reading - Shen and Kong – Ch. 4
Willebrord Snellius
(1580–1626) was a Dutch astronomer and mathematician
Image in the Public Domain

## Slide 2
Refraction
Refraction involves a change in the direction of wave propagation due to a change in propagation speed. It involves the oblique incidence of waves on media boundaries, and hence wave propagation in at least two dimensions.
Water Waves
E&M Waves
Waves refract at the top where the water is shallower
Image by NOAA Photo library http://www.flickr.com/photos/noaaphotolib/5179052751/ on flickr

## Slide 3
Oblique Incidence at Dielectric Interface
Transverse
Electric Field
Transverse
Magnetic Field
Ei
Et
Et
Ei
Er
Er
Hi
Hi
Ht
Ht
Hr
Hr
•
y

## Slide 4
Partial TE Analysis
Tangential E must be continuous at the boundary z = 0 for all x and for t.
This is possible if and only if and
The former condition is phase matching
Ei
Et
Er
Hi
Ht
Hr
•
y
z = 0

## Slide 5
Snell’s Law
SNELL’S LAW
•

## Slide 6
Snells Law via Phase Matching
Following phase continuity, the phase-front separation L is common to both the incident and transmitted, or refracted, waves.
λ1
λ2
L
θt
θi

## Slide 7
Snell’s Law Diagram
Tangential E field
is continuous …

## Slide 8: Refraction in Suburbia
Think of refraction as a pair of wheels on an axle going from a sidewalk onto grass. The wheel in the grass moves slower, so the direction of the wheel pair changes.
Note that the wheels
move faster (longer space)
on the sidewalk, and slower
(shorter space) in the grass.
Notes: 8

## Slide 9
Snell’s Law and Lenses
Surface
Normal
Bend towards normal
Bend
away from normal
glass
Image in the Public Domain

## Slide 10
Snell’s Law describing refraction was first recorded by Ptolemy in 140 A.D
First described by relationship by Snellius in 1621
First explained in 1650 by Fermat’s principle of least time.
History of Snell’s Law
BEAM OF LIGHT IS OFFSET AS IT PASSES THROUGH A TRANSPARENT BLOCK
MIRAGE
FOCUSING OPTICAL SYSTEM
NEAR THE HORIZON, THE APPARENT SUN IS HIGHER THAN THE TRUE SUN BY ABOUT ½ DEGREE
EXAMPLES:
Light from sky
Hot road or sand
Atmosphere
To apparent sun
Light path
To true sun
Earth

## Slide 11
Fermat’s Principle of Least Time
Fermat’s principle of minimum time argues that light will travel from one point to another along a path that requires the minimum time.
Applied to Reflection
•
A
B
B’
•
•
Since it is straight, the blue path is the shortest path from A to B’. So, the blue path is also the shortest reflecting path to B since it images the path to B’. For the blue path, the incidence and reflection angles equal.

## Slide 12
Fermat’s Principle of Least Time
Refraction
The time require for light to travel from A to B is given by
From , it follows that
•
•
A
B

## Slide 13
Total Internal Reflection
Beyond the critical angle, , a ray within the higher index medium cannot escape at shallower angles
For glass, the critical internal angle is 42°
For water, it is 49°
42°
INCOMING RAY HUGS SURFACE
TOTAL INTERNAL REFLECTION
Image is in the public domain

## Slide 14
Snell’s Law Diagram
Tangential E field is continuous …
Refraction
Total Internal Reflection

## Slide 15
Critical angle (diamond/air interface): sin-1(n2/n1) = sin-1(1/2.42) ~ 24°
Critical angle (glass/air interface) is: ~ 42°
Applications of Total Internal Reflection
Diamonds sparkle as light bounces inside them multiple times due to the high index of refraction
Critical
Angle
Image by Steve Jurvetson
http://en.wikipedia.org/wiki/File:Apollo_synthetic_diamond.jpg on Wikipedia

## Slide 16
Moreover, this wheel analogy is mathematically equivalent to the refraction phenomenon. One can recover Snell’s law from it: n1 sin θ1 = n2 sin θ2 .
The upper wheel hits the sidewalk and starts to go faster, which turns the axle until the upper wheel re-enters the grass and wheel pair goes straight again
Total Internal Reflection in Suburbia

## Slide 17
Waveguide Transports Light Between Mirrors
So what kind of waveguide are the optical fibers ?
Metal waveguides
Dielectric waveguides
Image by Dan Tentler http://www.flickr.com/
photos/vissago/4634464205/ on flickr

## Slide 18
Single Mode Fiber Structure
Light Propagating Through
A Multimode Optical Fiber
Optical Fibers
Modal dispersion is a distortion mechanism occurring in multimode fibers and other waveguides, in which the signal is spread in time because the propagation velocity of the optical signal is not the same for all modes
Core
8 μm
Cladding
125 μm
Buffer
250 μm
Jacket
400 μm
Step Index Fiber
Graded Index Fiber
Singlemode Fiber
125 μm
125 μm
125 μm
200 μm
50-100 μm
10 μm
Index of refraction
Input pulse
core
cladding
Acceptance
angle

## Slide 19: Fiber to the Home
Small Businesses
Splitter
OLT
(located in Verizon's central switching office)
ONT
Splitter
ONT
ONT
Splitter
ONT
ONT
Splitter
2.4 Gbps shared by up to 128 users
2.4 Gbps out
1.2 Gbps in
10-100 Mbps service rates
20 km reach
1
2
3
4
1
4
2
3
Time Division Multiplexing
ONT
ONT
ONT
An ONT (Optical Network Terminal) is a media converter that is installed by Verizon either outside or inside your premises, during FiOS installation. The ONT converts fiber-optic light signals to copper/electric signals. Three wavelengths of light are used between the ONT and the OLT (Optical Line Terminal):
• λ = 1310 nm voice/data transmit
• λ = 1490 nm voice/data receive
• λ = 1550 nm video receive
Each ONT is capable of delivering:
Multiple POTS (plain old telephone service) lines, Internet data, Video
Image by Raj from Chennai, India
http://commons.wikimedia.org/
wiki/File:Strings_of_lights.jpg
on Wikimedia Commons

## Slide 20: Fiber to the Home
Power &
Battery
ONT
Video
Data
POTS
ONT
1310 nm
1490 nm
Downstream
Upstream
Voice and Data
1550 nm
Video
Bandwidths & Services
Voice and Data
Channels downstream to each home
  λ = 1490 and λ = 1550 nm
Channel upstream from each home
  λ = 1310 nm
Image by uuzinger http://www.flickr.com/photos/uuzinger/411425452/on flickr
Image of ONT by Josh Bancroft http://www.flickr.com/photos/joshb/87167324/ on flickr
Image by uuzinger http://www.flickr.com/photos/uuzinger/411425461/ on flickr

## Slide 21
Transmission
Wavelength (nm)
1310
1490
1550
Upstream
Downstream
Passive Optical Network (PON)
Channels downstream to each home
  λ = 1490 and λ = 1550 nm
Channel upstream from each home
  λ = 1310 nm
Optical Assembly
Single mode
fiber
Ball lens
Thin film filters
TO Can PINS
TO Can Laser

## Slide 22
Separating Wavelengths
Dispersion
Diffraction
Image by Ian Mackenzie http://www.flickr.com/photos/madmack/136237003/
on flickr
Image by wonker http://www.flickr.com/photos/wonker/2505350820/ on flickr
Image is in the public domain
Sunlight diffracted through a 20 μm slit

## Slide 23
Fabry-Perot Resonance
Fabry-Perot Resonance: maximum transmission
minimum transmission
Wavelength [μm]
Transmission

## Slide 24
General concept of a MEMS Fabry-Perot filter formed on a detector
(by applying voltage between the top and bottom mirror the distance L between the mirrors can be adjusted)
Light in
Light out
General concept of a Mach-Zehnder Modulator
(phase shifters change the phase of the light beam in one of the waveguide arms with respect to the other beam, so that they can constructively or destructively interfere)
Phase Shifter
Phase Shifter
Flexible Membrane
Top Mirror
Silicon
Readout
Detector
Bottom Mirror
Membrane
Support

## Slide 25
MIT OpenCourseWare
http://ocw.mit.edu
6.007 Electromagnetic Energy: From Motors to Lasers
Spring 2011
For information about citing these materials or our Terms of Use, visit: http://ocw.mit.edu/terms.